# Fusion 360
Fusion 360 is and Autodesk product for CAD CAM. It is free (as in beer) for students, educators and start-ups. Fusion360 is used by The Edge programming staff when parametric design is an important requirement of a delivery or engagement. We use parametric design to re-use designs, mainly changing material dimensions (thickness), tooling and design scaling.
For example of internal work done with fusion 360 check out.
- Milkcrate Shelving
- Asgard Stool
- Laptop storage boxes
## Installation
Fusion 360 can be installed either with a web streamer (a small application that then downloads the full install) or from a full download. As the app is updated frequently, and most updates break backward compatibility we often have installs that are out of sync, leaving files un-openable. Fusion360 by default also installs for one user only.
For these reasons we recommend using the full admin install, and download the latest version which can always be found here[1)]. Install it from an admin command prompt with;
[1)] For more detailed instructions on lab usage consult this document. advanced_fusion360_lab_installation_instructions_en-gb.pdf
  "Fusion 360 Admin Install.exe" --globalinstall
## Tips and Tricks
### Parametric Design
The tips to successful parameter usage, that is avoiding the dreaded “Over Constrained” errors.
Make sure that your parameters are controlling only a single dimension at a time. For example - a rectangle that has a length, width is fine. But if you add a curve with a radius that intersects two edges, and then dimension that curves radius... you have a problem because the radius limits how far apart the sides can be.