### Make the Joule thief circuit
The coloured circuit diagram has holes to take the parts of the circuit (you can push out any hanging chads with a pen).
#### Start with the transistor
The transistor is the small black thing with 3 legs. It goes in the blue holes.
 Like the LED, the transistor only works when it is attached in the right orientation. If you pick it up, you will feel that it has a flat side, and a curved side (just like the blue diagram).
 Insert the transistor so the curved side matches the blue picture (you might need to separate the legs a bit first).
 In the picture below, this means the curved side is at the top.

 Push the transistor down so it is close to the surface of the circuit board, and bend the legs apart at the back to hold it in place.
#### Then add a resistor
Now find the resistor - this only has two legs, and it works which ever way you put it in. Resistors can be brown or blue, and have stripes.

Bend the legs a bit, and insert them through the brown holes. Push it down onto the board, too.

When you look at the back of the circuit board, two wires are now adjacent: the middle one from the transistor and one from the resistor.
 Twist these wires together as close to the board as possible. Then fold the twisted pair over and make sure they do not touch any other wires.

#### now add the wound toroid
The printed circuit has a place for the toroid, outlined in green. take the plain single wire, and push the end through the hole at the end of the outlined green line.

 Look on the back, and you will see this wire is beside the other leg of the resistor. Twist these two together.

 The striped single wire from the toroid follows the solid green line, and pushes through next to a transistor leg.
 Insert the striped wire, and twist these two together (bend them away so nothing is touching).

 The joined toroid wires go through the hole at the bottom on the diagram, and can hang free until the next step.

Attach the LED
There are two orange holes left on the circuit diagram, one of them labelled ‘long’.
Have a look at the LED, and you will see one leg is longer than the other – this long leg goes through the ‘long’ hole.
Turn the circuit over, and twist the LED legs together with the wire or wires beside them.

Attach the Lemon Battery
The circuit has two holes to take the wires from the lemon battery – one is red, the other is black. Insert the bared ends of the wires you have attached to the lemon battery electrodes, and twist with the adjacent wires.

Below is what the twisted wires should look like – bent apart so they do not touch (ignore the motor).

### Winding the toroid – if you need to.
The ring shaped object in your kit is actually a magnet, called a toroid. To make it work in this circuit, it needs to have two strands of wire wrapped around it.
 Using paired wire makes it easy to avoid having overlapping wires, which would stop it from working.
First, cut a length of paired wire about 210mm long. It is easiest to strip both ends of the wires at this stage, but this can also be done later.
 To start the winding, thread the toroid onto the wire, about 3cm from one end, and bend the wire around as shown below:

 Now take the long end of the wire, while keeping hold of the toroid with your other hand, and loop the wire back through the centre of the toroid.
 Then, pull the wire tight.

 Continue threading the wire through, until there are 5 loops around the toroid. More loops actually reduces the effectiveness of this device, and it will still work with 4.

When you have finished 4 or 5 loops, you can trim the ends of the wire to about 3cm if necessary (scissors will work).

If it has not been done for you, separate the protruding wires (use a knife or cutters, or just pull them apart with your fingers).
 Do this on both ends.

If the ends of the wires have not been stripped, do it now. Look closely and you will see one wire has a black stripe, while the other is all white (or grey).
 Take a plain wire from one side of the wound toroid, and a black striped wire from the OTHER side, and twist them together.
 You end up with this: